## Slide 1: WHAT IS QUALITY ASSURANCE?
Contractors Transportation Management Association
2017 Workshop, Point Clear, Alabama, May 23-26, 2017
Click to edit Master text styles
Roberta Riel
Work sponsored by U.S. Department of Energy Office of Packaging and Transportation (EM-4.24)
Nuclear Engineering Division
Argonne National Laboratory

## Slide 2: Outline
What is quality assurance?
P-D-C-A Cycle
Everyday examples
Examples of PDCA for packaging
Failures of quality assurance
Inspections, audits, and assessments
Graduate Certificate in Nuclear Packaging
Summary

## Slide 3: Quality Assurance
“Quality assurance (QA): Planned and systematic activities necessary to provide adequate confidence that the product or service will meet the given requirements.”
–The Certified Quality Manager Handbook, Quality Management Division, American Society for Quality, pg. 159 (1999)
Can provide checks and balances within a corporation to ensure ethical behavior

## Slide 4: Quality Assurance
“Quality assurance is too expensive.”
–Every manager

## Slide 5: Why Quality Assurance?
Provides assurance that product or service meets requirements
  Can product/service provide what is expected by customer?
Provides for reproducibility of product or service
  Every product/service is the same
  For science, can assure reproducibility of results (cold fusion)
Provides documentation for legal actions
  Lawsuits
  Recalls
  Documentation can be a double-edged sword
Bottom line: SAVES MONEY

## Slide 6: Plan-Do-Check-Act (PDCA) Cycle
Shewhart (Plan—Do—Check—Act)
Deming (Plan—Do—Study—Act)
Plan
Do
Check
Act

## Slide 7: PDCA Cycle
Provides a framework for quality assurance
  Easy-to-follow process for all workers at all levels
  Documentation can ease loss of knowledge/experience
Provides for continuous process improvement
  “Act” step can help to correct problems before manufacturing
Used extensively in manufacturing in Japan in 1970’s
  Deming’s PDSA cycle used by Japanese automakers

## Slide 8: Everyday Examples
Dinner
  Plan—What do I want?
  Do—What will I prepare?
  Check—Do I have the necessary food?
  Act—If not, buy the necessary food
Travel
  Plan—Where do I want to go? What is my budget?
  Do—Make travel plans
  Check—Do I have enough vacation time? Money?
  Act—Arrange for vacation/money
Budget
  Plan—I make $XX a week
  Do—Create budget ($X a week for required expenses)
  Check—Do I have enough $ to meet expenses?
  Act—Revise budget as necessary to meet required expenses

## Slide 9: Examples of PDCA for Packaging
Suppliers and sub-tier suppliers
  Plan—Who can provide the necessary supplies?
  Do—Prepare procurement documentation
  Check—Can the supplier meet the requirements? Inspect during manufacture?
  Act—Place procurement and inspect upon receipt
Design packaging
  Plan—What is the purpose of the packaging?
  Do—Design packaging to meet purpose/needs
  Check—Perform required testing (welds, accident)
  Act—If necessary, redesign/rework to meet design requirements
Test packaging
  Plan—What tests are required?
  Do—Perform testing
  Check—Did packaging meet requirements?
  Act—If necessary, redesign/rework to meet testing requirements

## Slide 10: Failures of Quality Assurance (1/4)
In 1972, a Ford Pinto exploded upon rear impact (1 fatality, 1 serious injury)
Injured plaintiff (13-year-old child) sued Ford and was awarded $2.5 million in compensatory damages and $125 million in punitive damages
In 1968 Ford designed the subcompact Pinto
  Goal to build a car that weighed <2000 lb. that could sell for <$2000
  Goal resulted in fuel tank being placed over rear axle (Japanese and European designs); this allowed only 9–10 in. of “crash” space, there was no reinforcing structure, and an exposed flange and bolt heads could puncture the tank
  Crash tests showed that Pinto could not meet safety requirements
  If Ford corrected these deficiencies, it would have added $15.30 to the car’s cost
  Ford decision-makers went ahead with flawed design
Added cost of $15.30 vs. multi-million dollar judgments
  Short-term savings vs. long-term costs (damages, recall costs, etc.)
(Grimshaw v. Ford Motor Co., Civ. No. 20095, May 29, 1981)

## Slide 11: Failures of Quality Assurance (2/4)
Recent Takata airbag recall
  14 deaths and more than 100 injuries due to faulty airbags
  In 1998, Takata made a change, using ammonium nitrate as propellant (cheaper but less stable)
  In 2015, Takata admitted there was “widespread danger of its air bags exploding and sending metal shrapnel flying at passengers”
  In May 2016, investigators identified the ammonium nitrate as the “root cause” of the failures when the propellant is exposed to humid air
  Takata cannot manufacture enough airbags for the scope of the recall (100 million vehicles worldwide)
  “Just-in-time” recall over 3 years, starting with oldest air bags in hot-test climates to be recalled first
  Expected to take until 2019 to complete recall
  Up to 70% of replacement air bags not manufactured by Takata
  (Quality Progress, American Society for Quality, pp. 10–11, August 2016)
In January 2017 (from CNN.com), three former executives indicted; $1 billion fine against Takata

## Slide 12: Failures of Quality Assurance (3/4)
Volkswagen 2.0-L TDI diesel engine vehicles in the United States
  Approximately 460,000 2.0-L four-cylinder diesel vehicles affected
  Government regulations limit the use of engine software that reduces the effectiveness of a vehicle’s emissions control systems. Those are the “defeat device” regulations. Volkswagen did not comply with those regulations with respect to the 2.0-L TDI vehicles identified in the EPA’s September 18, 2015, notice and subsequent November 2, 2015, notice regarding 3.0-L TDI vehicles
Subject to final approval by the court, the settlement agreements submitted on June 28, 2016, resolve civil claims regarding approximately 460,000 Volkswagen 2.0-L TDI diesel engine vehicles in the United States. Volkswagen has agreed to the following:
  Vehicle buybacks and lease terminations, approved emissions modifications, and cash payments to affected customers
  Establishing a $2.7-billion environmental remediation fund and invest $2.0 billion in initiatives to promote the use of zero-emissions vehicles in the United States
  Resolution of existing and potential state consumer protection claims related to the diesel matter with the attorneys general of 44 U.S. states, the District of Columbia, and Puerto Rico
(https://www.vwdieselinfo.com/faqs/)

## Slide 13: Failures of Quality Assurance (4/4)
NRC CoC Violation
  DOE (Los Alamos National Lab, LANL) procured Optional Shield Inserts from the cask designer, Energy Solutions (ES). The license drawings, C-038-145083-004-2 Rev. 1 (Shield Insert A) and DWG-LIN-201588-ME-0002-02 Rev. 0 (Shield Insert B) both require in Notes 18 and 16, respectively, that “ALL FASTENERS MUST BE MANUFACTURED IN THE U.S.A. HEAD MARKINGS SHALL BE VERIFIED AGAINST THE LATEST D.O.E. CHART, ENERGY SOLUTIONS SUPPLIED”
  The fabricator to Energy Solutions procured fasteners that were manufactured outside of the United States, and performed a commercial grade dedication to justify the use of the fasteners. The shield inserts were accepted and delivered by Energy Solutions to LANL and accepted by LANL. DOE (Idaho National Lab, INL) consigned the packages for shipment with these shield inserts. Some time later, Energy Solutions discovered the fastener issue and notified LANL and INL on August 18, 2016
  DOE (INL) is preparing a §71.95 report to NRC, since DOE consigned NRC-certified packages for shipment that did not meet the CoC license drawing requirements (§71.95(a)(3))
  Sub-tier fabricator to primary supplier tried to save money
  Final resolution—still pending

## Slide 14: Inspections, Audits, and Assessments (1/2)
Inspections
  A formal review of in-process manufacturing
  NRC inspections
Audits
  A formal review of documentation and implementation of a quality assurance program
  Internal and external (sometimes called a “third-party” audit)
  DOE audits
Assessments
  Multiple types: self-assessment, management assessment, independent assessment
  Less formal than inspections and audits
  ISO assessments

## Slide 15: Inspections, Audits, and Assessments (2/2)
Inspection or Audit Team
  Formal qualifications, plan(s) including scope, and schedule(s)
  May be internal or external
  Formal checklist(s)
  Formal opening and closing meetings
Auditee
  Review qualifications
  Agree with plan and schedule
  Establish reporting
  Establish process with team regarding disagreements
Inspector/Auditor
  Will document what is said…so…
  Silence is an inspector’s/auditor’s best friend

## Slide 16: Packaging Quality Assurance
DOE QA
  DOE Order 414.1D (10 criteria, performance-based)
NRC QA for Packaging
  10 CFR 71, Subpart H (18 requirements, compliance-based)
  NRC Regulatory Guide 7.10, Revision 3 (June 2015)
DOE-EM Office of Packaging and Transportation (EM-4.24)
  DOE Order 460.1D (December 2016)
Industry Standards
  ASME NQA-1 (NRC endorses 2008 with 2009 Addenda version)
  ISO 9001

## Slide 17: Graduate Certificate in Nuclear Packaging
DOE-EM/PCP Packaging University
University of Nevada, Reno, Graduate Certificate in Nuclear Packaging (GCNP)
  9 credits total
    3 required courses (ME 691, ME 692, and ME 695)
    6 electives
    Requires a B average
Argonne National Laboratory courses
  ME692 Quality Assurance (March 20-24, 2017)
  ME691 ASME Pressure Vessel Code (June 19-23, 2017)
  ME694 Nuclear Transport Security (September 11-15, 2017)
More information can be found at: https://rampac.energy.gov/home/education/packaging-university

## Slide 18: Summary
Quality assurance is not a separate function
Quality assurance must be built into daily life
Quality assurance affects everyone, from CEO/president down to line worker
Quality assurance may have up-front costs, but the end costs of recalls, reconstruction/refabrication, damages with associated legal costs, and loss of public respect can be devastating
DOE and NRC requires quality assurance for packaging
PCP Packaging University and UNR GCNP are additional educational resources

## Slide 19: Acknowledgments
This work is supported by the U.S. Department of Energy Office of Environmental Management, Office of Packaging and Transportation, Packaging Certification Program, under Contract No. DE-AC02-06CH11357.